## Slide 1: Radio Part 2
Lesson 29

## Slide 2: What The Lesson Will Cover
Recap the role of channel numbers in radio transmissions
Program a micro:bit to send a message through the radio hardware
Program a micro:bit to receive a message through the radio hardware
Create and send your own messages
Use selection to enable the micro:bit to send different messages when different buttons are pressed

## Slide 3: Channel Numbers
Radio transmits or broadcasts, which means that anyone nearby with a micro:bit can receive the data
Addressing is used to send the data to a particular micro:bit or group of micro:bits, without others seeing the data
Addressing uses channel numbers where the radio is ‘tuned’ to a specific channel between the range 0 to 100
The radio module allows you to set the channel using the code radio.config(channel=19)– this sets the radio to channel 19
The micro:bit still receives broadcasts but filters out the messages that do not match your specific channel number
If you don’t set a channel number your micro:bit will receive every broadcast from every micro:bit
Notes: Recap addressing and channel numbers

## Slide 4: Sending your own message
# Add your Python code here.
# radio 1
from microbit import *
import radio
radio.on()
radio.config(channel=5)
while True:
if button_a.was_pressed():
my_message = "Hi"
radio.send(my_message)
sleep(200)
The program code is similar to the sender program used in last lesson
This time the program uses a variable called my_message which stores your message, you can change this
There are no trigger words used, the message from one micro:bit is sent as data, to another micro:bit
The while loop ensures that the message is sent every time that Button A is pressed
Notes: Talk over the sending a message program before Learners try it out

## Slide 5: Activity
You are now going to complete the activity task where you will send a message to and from one micro:bit to another
You need to pair up with another student
Decide which student will be the sender and which will be the receiver
Decide which channel number you are going to use
The sender student completes program one
The receiver student completes program two
Using selection to add additional messages that can be sent
Notes: The teacher may want to decide the channel numbers beforehand to avoid Learners sending and receiving unwanted messages.