## Slide 1: The Temperature Sensor
Lesson 23

## Slide 2: What You Will Learn
How the micro:bit can be used to take temperature readings
Create program that displays the temperature
How to adjust the accuracy of the reading
Program a real time temperature sensor

## Slide 3: The Temperature Sensor
The micro:bit module gives you access to all the hardware that is built into your board
This includes a temperature sensor which can be used to take readings of the immediate surrounding area
The reading saved can be stored in a variable and then displayed on the LEDs
The program code is simply temperature()
This returns the temperature of the micro:bit in degrees Celcius
Notes: Explain the basics of the temperature sensor

## Slide 4: Taking a Reading
The thermometer on the micro:bit is embedded in one of the microchips
The chips warm up when you power them up
The processor chip – in the green star – also produces a lot of heat
Consequently, you have to adjust the reading to get an accurate measure of the room temperature
Notes: Show the location of the sensor, ask Learners to find it on their micro:bits
Explain that the temperature reading needs to be adjusted to account for the chip heat

## Slide 5: Taking a reading
from microbit import *
while True:
if accelerometer.was_gesture('shake'):
display.scroll(temperature())
Notes: Learners / teacher talk through the program, what does it do, when does it run, how do you control it?
Learners copy up the code, this is part of Activity one

## Slide 6: Current temperature reading
24
Notes: Change the 24 to the current temperature of the room so that Learners can adjust their program